ISOLDE RILIS upgrade (priority 1)

- Extension of laser hut including entry porch and RF shielding

- RF measurements by TIS/GS: noise up to 100 MHz

- plans for metal shielded hut ready

- electricians will prepare for reconstruction in week 3/2001

- METAREG ready to do construction in February 2001

- final cost estimate in week 3/2001  (preliminary estimate 50 kCHF)

- netfilter can be provided by Uni Mainz (ISOLDE Collaboration contribution)

- honeycomb feedthroughs for ventilation to be ordered immediately (1842 CHF)

- Fiberswitch for multiplexing 3 inputs to wavemeter

- Uni Mainz just ordered a fiberswitch, but there are alternative suppliers

- wait for practical experience in Mainz and order afterwards (spring 2001)

- costs: about 5 kCHF (+x for single mode input fibers)

- Beam diagnostics

- CCD camera sensitive from 210 to 850 nm

- 3 remote-controlled beam shutters plus attenuators

- digitalizer of video signal (VME module from SL/BI)

- analysis of beam profile on VME base (PS/CO)

- costs estimated to 15+x kCHF (depends strongly on type of CCD camera)

- Remote-controlled beam tuning

- 6 picomotor mounts 8807 from Newfocus (7029 USD = 12512 CHF)

- multi-axis driver from Newfocus (4675 USD = 8322 CHF)

- best solution if compatible with CVL noise (order test sample?)

- 2 large aperture automatic shutters (ca. 4 kCHF)

- programmable loop for feedback with beam profile monitor (PS/CO)

- Optimize frequency doubling system (BBO)

- adapt focussing optics: tests required for optimization (ca. 3 kCHF)

- tests for final design and installation during 2001

- temperature controlled BBO holder (use CTF design?)

- Adapt CVL-RF system to optimize thyratron lifetime

- little costs but support from PS/RF required

ISOLDE RILIS upgrade (priority 2)

- Improvement of CVL beam guidance

- closed tubes and adapted holders for beam splitters and mirrors

- prototype developed by ATRIX (ca. 55 kCHF total)

- 2001 final design and ordering, early 2002 installation

- Automatized dye laser control

- 2 new remote controlled dye lasers plus 2 dye amplifiers (ca. 38 kCHF)

- 11 dye laser power monitors plus multi-channel readout (ca. 20 kCHF)

- items could be ordered soon, but presently postponed for budget reasons

- support for readout (together with 2. fiberswitch) and feedback from PS/CO